## Slide 1: Introduction Practical Session 3: Image processing 1
Sebastian Amador Sanchez
sebastian.amador.sanchez@vub.be
Anass Hamdi
anass.hamdi@vub.be

## Slide 2: Content
Usage of SimpleITK
Introduction to 3D Slicer
Practical session 3

## Slide 3: Usage of SimpleITK

## Slide 4
A simplified version of ITK (Insight Tool Kit) for scientific image processing, segmentation, and registration
Ideal for medical imaging: X-rays, CT, PET, MRI, and US
Available in Python:
  pip install SimpleITK | conda install simpleitk

## Slide 5: Image fundamentals
An image in SITK than in cv2 or scikit-image
  SITK = set of points on a grid occupying a physical region in the space
  Others = array
SITK takes into account:
  Pixel/voxel spacing information
  Location in the physical space

## Slide 6
512
512
256
256
Image spacing = (1.0, 1.0)
Image spacing = (0.97, 2.0)
Image spacing:

## Slide 7
Image origin and direction:
Image origin = (-136.3, -20.5)
Orientation matrix = (0.7, -0.7, 0.7, -0.7)
Image origin = (16.9, 21.4)
Orientation matrix = (1, 0, 0, 1)

## Slide 8
Image registration:
Image segmentation:

## Slide 9: How to read an image?
import SimpleITK as sitk
image = sitk.ReadImage(path_to_image)

## Slide 10: Conversion between SimpleITK and NumPy
From SimpleITK to NumPy:
image = sitk.ReadImage(path_to_image)
array = sitk.GetArrayFromImage(image)
  array.shape -> (155, 240, 240)

## Slide 11: Reading an image
Multiple image formats:
  Standard ones: .jpeg, .png, .tiff, etc
  Medical ones: .mha, .nii, .dcm
image = sitk.ReadImage(path_to_image)
  Default = '16-bit signed integer’
image = sitk.ReadImage(path_to_image, sitk.sitkUInt8)

## Slide 12: Introduction to 3D Slicer

## Slide 13: 3D Slicer
3D medical image viewer
Analyze medical images and their metadata
Create 3D reconstructions of segmentations
Modules available for medical image analysis:
  Registration
  Segmentation
  …

## Slide 14: https://download.slicer.org/

## Slide 15: How to use for the exercises
Easy and quick way for viewing slices in all 3 orientations at once
Use 3D Slicer to select a suitable slice to plot 2D results for exercises
Alternative to 3D Slicer (or any 3D image viewer): Manually plot slices in python with matplotlib  slow and time-consuming

## Slide 16: Example
Data probe in bottom left contains voxel information:
  (Location in physical space)
  (Intensity value)
  Location in image space
Use image space location to choose slice for exercises
Remember: NumPy inverts the axis order! (XYZ  ZYX)

## Slide 17: Practical Session 3
Image enhancement and denoising

## Slide 18: Image enhancement & denoising
Image histogram
Image denoising:
  Mean, median, and Gaussian filtering
Image denoising:
  Homomorphic Unsharp Masking filter
Grading:
  10 points code/figures
  10 points oral evaluation

## Slide 19: Exercise 1: Image histogram
Linear stretching *
Histogram equalization *
CLAHE (skimage implementation)

## Slide 20: Exercise 1: Image histogram
Linear stretching *
Original
Linear stretched

## Slide 21: Exercise 1: Image histogram
Histogram equalization*
Bins centers
Scaled cumulative
distribution

## Slide 22: Exercise 1: Image histogram
Histogram equalization*
Interpolate
Original
Equalized

## Slide 23: Exercise 1: Image histogram
To report:
  A comparison between approaches.

## Slide 24: Exercise 2: Image denoising
Mean filter *
Gaussian filter
Median filter

## Slide 25: Exercise 2: Image denoising
Mean filter *
Convolve

## Slide 26: Exercise 2: Image denoising
To report:
  The filtered images, noise filtered, remaining noise, and edge images.
  The root mean squared error (RMSE) between filtered and original images.

## Slide 27: Exercise 3: HUM algorithm
Remove bias noise

## Slide 28: Exercise 3: HUM algorithm
Direct implementation *:
  Get mean intensity (global)
  Define a window of 20 x 20 x 20
  Get mean intensity (local)
  Compute HUM
  Move the window, and repeat
20
20
20

## Slide 29: Exercise 3: HUM algorithm
Pad image *:
  Pad the image
  Get mean intensity (global)
  Define a window of 20 x 20 x 20
  Get mean intensity (local)
  Compute HUM
  Move the window, and repeat
20
20
20

## Slide 30: Exercise 3: HUM algorithm
Pad + threshold *:
  Pad the image
  Filter pixels below a threshold (10)
  Get mean intensity (global)
  Define a window of 20 x 20 x 20
  Get mean intensity (local)
  Compute HUM
  Move the window, and repeat
20
20
20

## Slide 31: Exercise 3: HUM algorithm
To report:
  Filtered images
  NRMSE and SSIM between filtered and original images